#### Press release

Obersulm, Germany 11/28/11

# USB 3.0 offers new perspectives in machine vision

IDS presents first multi-camera system

with eight USB 3.0 industrial cameras

IDS Imaging Development Systems GmbH presents the world’s first multi-camera system with eight USB 3.0 cameras. Each of the eight newly developed USB 3 uEye CP cameras equipped with a highly sensitive 1.3 Megapixel e2v sensor delivers 25 frames per second. This results in a total data rate of 250 MByte, which are transferred via one single USB 3.0 cable to the host PC. Despite this enormous data rate the CPU load is a mere 20%.

Hence, it is rather easy to implement multi-camera systems with the new IDS USB 3.0 camera. The camera is not only perfect for common industrial applications, but especially for multi-camera and 3D systems. These could previously only be implemented using costly and expensive solutions with either Camera Link or Firewire.

More than 9 years of experience in the development and sale of USB cameras has consistently been implemented in the new camera family. The 29 x 29 x 29 mm camera housing is not only compact, but due to its magnesium casing also very lightweight and robust. The new USB 3 uEye CP offers trigger, flash and pulse width modulation as well as two GPIOs (General Purpose I/O). The GPIOs can be converted into a serial port (RS232), e.g. to trigger peripheral devices. Thanks to the lockable micro USB 3.0 and Hirose connectors the camera is also perfect for rough environments. With a power consumption of just 1 Watt, the camera can easily be integrated into embedded or mobile applications.

The USB 3 uEye CP boasts a range of outstanding features: Brightness corrections are realized by a comfortable 12-bit lookup table and hardware gamma. 12-bit color depth offers a by factor 16 increased level of detail compared to the usual 8 bit. Hardware based data preprocessing and color calculation saves additional PC resources.

Initially the USB 3 uEye CP family will be offered with three different CMOS sensors. These include a highly sensitive 1.3 Megapixel e2v sensor, as well as a WVGA and a high resolution 5 Megapixel sensor from Aptina. More high resolution sensors will follow in 2012.

The new SuperSpeed USB 3.0 interface offers a data rate of 400 MByte/s and hence a significant advantage compared to common interfaces. It goes without saying that IDS’ own proven software package for all common operating systems also supports the new

USB 3 uEye CP camera family. Hence, mixed operation of USB 2.0, USB 3.0 and GigE cameras is a breeze. The universal availability of USB as a mainstream interface guarantees long-term investment security.

Detailed information and videos regarding the multi-camera system are available via www.ids-imaging.com/usb3.

Image:

USB 3 uEye CP camera

Press contact:

IDS Imaging Development Systems GmbH

Bettina Ronit Hoermann

Technical Communication

Dimbacher Str 6-8

74182 Obersulm, Germany

Tel: +49 7134 961 96-154

Fax: +49 7134 961 96-99

Email: b.hoermann@ ids-imaging.de

Web: www.ids-imaging.de

Company profile:

IDS Imaging Development Systems GmbH is a leading manufacturer of industrial cameras with 14 years of experience. Founded in 1997, IDS started with the development and distribution of frame grabber cards, which became the cornerstone of success. In 2004 IDS launched their first self-developed industrial cameras known as uEye®. Today nearly 200,000 uEye cameras with USB or Gigabit Ethernet interface are in use in areas like industrial automation, quality assurance, and medical technology as well as in non-industrial applications. IDS offers a modular system for sensors, housing and interfaces with more than 1200 variants currently available. Additionally, IDS stands for customer-specific solutions, long-term product availability and excellent quality "Made in Germany". For the surveillance and security market, IDS offers IP-cameras and iGuard – a flexible video management software. More than 100 staff are currently employed in the areas of development, manufacturing, administration, sales and support at the IDS headquarters in Obersulm, Germany. Apart from own sales offices in the US, Japan and France, IDS cooperates with a worldwide network of distributors.