IDS expands its portfolio with CMOS sensors from ON Semiconductor

High speed for your vision system

The latest industrial camera generation USB 3 uEye CP from IDS is now available with the CMOS sensors PYTHON 500, PYTHON 2000 and PYTHON 5000 from ON Semiconductor. In addition to the fully-established PYTHON 1300, IDS Imaging Development Systems offers three more members of the sensor series. The sensors are designed to provide high-speed, reaching more than 1,000 fps with AOI feature.

The global shutter sensors of the PYTHON series are available as colour or monochrome version. They include large and light-sensitive pixels with 4.8 µm.

Using the special AOI (Area of Interest) feature with horizontal and vertical read-out, the combination of USB 3 uEye CP camera from IDS and ON Semiconductor sensor reaches a top speed of more than 1,000 fps.

PYTHON 500 – the fastest

The UI-3130CP model with the PYTHON 500 sensor is IDS’ fastest camera in the optical class below 1 MP, providing more than 560 fps in full resolution (0.5 MP, 800 x 600 pixels). It is especially suitable for slow motion or high speed tracking applications.

PYTHON 1300 – successfully in use

The UI-3140CP model convinces with its EMVA1288 technical values​: due to low noise it is very well suited for machine vision applications. A dynamic range of 57.5 dB ensures high-contrast images. The 1/2'' sensor format and the resolution of 1.3 MP (1280 x 1024 pixels, 169 fps) are quite common in the market. They are used for a variety of inspection and quality assurance applications and are ideal for cost-effective C-Mount lenses.

PYTHON 2000 – more than Full HD

Providing a resolution of 1920 x 1200 pixels (2.3 MP), the UI-3160CP with the PYTHON 2000 is designed for use with Full HD (>180 fps), which meets the need of both classical industrial applications and visualization tasks. If required a change to the 4:3 format (1600 x 1200 pixels), that is common in the field of medical technology, is easily possible.

PYTHON 5000 – the largest

In the field of 1''-sized sensors, the new UI-3180CP with the PYTHON 5000 sets marks: it is the highest resolution camera in this optical class (5 MP) with global shutter, providing 5.3 MP (2592 x 2048 pixels, 68 fps). For different user’s requirements, both the square 2K x 2K format and Full HD is available. The combination of size and number of pixels makes it ideal for use in the field of microscopy, especially eye inspection applications which benefit from switching between AOI and full resolution.

ca. 2 400 char.

IMAGES

Sample application: eye inspection	USB 3 uEye CP with PYTHON sensor

### ABOUT IDS

Imaging Development Systems (IDS) is one of the leading global manufacturers of digital industrial cameras with USB 2.0, USB 3.0 or GigE interface. We serve the apparatus and mechanical engineering markets with comprehensive support and high-quality products that are “Made in Germany”. As an owner-managed company, we have subsidiaries in Japan and USA as well as further offices in Europe and Asia. We focus on the company’s sustainable expansion, supported by our distribution partners in almost every country in Europe and Asia, and by 200 motivated and qualified employees worldwide.

### PRESS CONTACT

IDS Imaging Development Systems GmbH
Jan Jordan
Product Communications/PR
Dimbacher Str. 6-8, D-74182 Obersulm, Germany
T: +49 7134 96196-154
F: +49 7134 96196-99
E: j.jordan@ids-imaging.de
Web: www.ids-imaging.com